BIOS Bootkits

---
Agenda
Leveraging user-space paths
Analyzing motherboards
Identifying peripherals
PCI, LPC, SPI Communication
Reading from the SPI Flash
The Reset Vector address
UEFI vs Legacy BIOS
UEFI Phases
Summary

---
Protection Rings
3
User Space
2
1
0
Kernel Space

---
EFLAGS Register
31
13 12
0
ID
VIP
VIF
AC
VM
RF
NT
IOPL
OF
DF
IF
TF
SF
ZF
AF
PF
CF
IOPL (I/O Privilege Level) - Indicates the I/O privilege level of the currently running program or task. The current privilege level (CPL) of the currently running program or task must be less than or equal to the I/O privilege level to access the I/O address space. The POPF and IRET instructions can modify this field only when operating at a CPL of 0.

---
I/O Instructions
IF ((PE = 1) and ((CPL > IOPL) or (VM = 1))) THEN
        IF (Any I/O Permission Bit for I/O port being accessed = 1) THEN
        #GP(0);
        ELSE
        DEST := SRC;
        FI;
ELSE (Real Mode or Protected Mode with CPL ≤ IOPL *)
        DEST := SRC;
FI;

---
How to set IOPL bits
In Linux, use the iopl(3) function
In Windows, use the NtSetInformationProcess(...) function
...

---
The Architecture
CPU
Memory
North Bridge
PCIe
South Bridge
LPC
SATA
PCI
Flash ROM

---
The Architecture
CPU
Memory
North Bridge
PCIe
South Bridge
LPC
SATA
PCI
Flash ROM

---
PCI Configuration MMIO Registers
31 30 29 28 27 26 25 24 23 22 21 20 19 18 17 16 15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
Bus
Device
Func
Offset
CFGE
CFGADR
0xCF8
31 30 29 28 27 26 25 24 23 22 21 20 19 18 17 16 15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
Value
CFGDAT
0xCFC

---
Example
Device(0x1, 0x2, 0x3), Register(0x4)
#include <sys/io.h>
#define CFGADR	0xCF8
#define CFGDAT	0xCFC
u32 adr;
adr = (1 << 31) | (0x1 << 16) | (0x2 << 11) | (0x3 << 8) | 0x4;
outl(adr, CFGADR);
u32 dat;
dat = inl(CFGDAT);

---
LPC Controller (00.1F.00)
Is at address 0x00, 0x1F, 0x00
Bus: 0x00
Device: 0x1F
Function: 0x00
Contains an interesting register called RCBA (0xF0)
Offset: 0xF0

---
Root Complex Base Address
RCBA (Root Complex Base Address Register) - 0xF0
31 30 29 28 27 26 25 24 23 22 21 20 19 18 17 16 15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
Base Address
EN
RCRB
Physical Memory

---
Root Complex Register Block
RCRB
Physical Memory
Contains SPI Registers (at offset SPIBAR)
Is mapped at some Physical address
/dev/mem in Linux
mmap syscall
Pointed by the RCBA which is in LPC Controller
The size is 16KB

---
SPI Base Address
SPIBAR (0x3800)
RCRB
SPIRB
Physical Memory
The offset starting from RCRB beginning
Points to SPI register block
Is a hard-coded offset (based on PCH, ICH etc. version)

---
Finding the SPI Register Block
u32 lpc_adr;
lpc_adr = (1 << 31) | (0x00 << 16) | (0x1F << 11) | (0x00 << 8) | 0xF0;
outl(lpc_adr, CFGADR);
u32 rcba;
rcba = inl(CFGDAT);
int mem;
mem = open(“/dev/mem”, O_RDWR);
void *rcrb;
rcrb = mmap(NULL, 0x4000, PROT_READ | PROT_WRITE, MAP_SHARED, mem, rcba & 0xFFFFC000);
void *spirb;
spirb = ((u8*)rcrb + 0x3800);

---
Finding the SPI Register Block
Read RCBA from the LPC Controller
u32 lpc_adr;
lpc_adr = (1 << 31) | (0x00 << 16) | (0x1F << 11) | (0x00 << 8) | 0xF0;
outl(lpc_adr, CFGADR);
u32 rcba;
rcba = inl(CFGDAT);
int mem;
mem = open(“/dev/mem”, O_RDWR);
void *rcrb;
rcrb = mmap(NULL, 0x4000, PROT_READ | PROT_WRITE, MAP_SHARED, mem, rcba & 0xFFFFC000);
void *spirb;
spirb = ((u8*)rcrb + 0x3800);

---
Finding the SPI Register Block
u32 lpc_adr;
lpc_adr = (1 << 31) | (0x00 << 16) | (0x1F << 11) | (0x00 << 8) | 0xF0;
outl(lpc_adr, CFGADR);
u32 rcba;
rcba = inl(CFGDAT);
int mem;
mem = open(“/dev/mem”, O_RDWR);
void *rcrb;
rcrb = mmap(NULL, 0x4000, PROT_READ | PROT_WRITE, MAP_SHARED, mem, rcba & 0xFFFFC000);
void *spirb;
spirb = ((u8*)rcrb + 0x3800);
Ask OS to give us a virtual address for that RCBA address

---
Finding the SPI Register Block
u32 lpc_adr;
lpc_adr = (1 << 31) | (0x00 << 16) | (0x1F << 11) | (0x00 << 8) | 0xF0;
outl(lpc_adr, CFGADR);
u32 rcba;
rcba = inl(CFGDAT);
int mem;
mem = open(“/dev/mem”, O_RDWR);
void *rcrb;
rcrb = mmap(NULL, 0x4000, PROT_READ | PROT_WRITE, MAP_SHARED, mem, rcba & 0xFFFFC000);
void *spirb;
spirb = ((u8*)rcrb + 0x3800);
Move RCRB by SPIBAR to get the SPI Registers

---
SPI Registers
HSFSTS: Hardware Sequencing Flash Status Register
HSFCTL: Hardware Sequencing Flash Control Register
FADDR: Flash Address Register
FDATAx: Flash Data Register [0..15]
...

---
 The HSFSTS (0x04) Register
15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
F LOCKDN
FDV
FDOPSS
S C I P
BERASE
AE L
FCERR
FDONE
SCIP: SPI Cycle In Progress. Set by the HW. Can be used to check the status
AEL: Access Error Log. Needs to be cleared. Can be used to check errors
FCERR: Flash Cycle Error. Needs to be cleared. Can be used to check errors
FDONE: Flash Cycle Done. Tells whether the operation is done or not
...

---
 The HSFCTL (0x06) Register
15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
F
SM
I
E
FDBC
F
C
Y
C
L
E
FGO
FDBC: Block count. The value is zero based.
FCYCLE: 0b00 is read and 0b10 is write
FGO: Start the operation
...

---
 The FADDR/FDATAx Registers
31 30 29 28 27 26 25 24 23 22 21 20 19 18 17 16 15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
FLA
FADDR
0x08
31 30 29 28 27 26 25 24 23 22 21 20 19 18 17 16 15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
Data
FDATAx
0x10+
FLA: Flash Linear Address
...

---
Reading from the Flash ROM
void *spirb;
spirb = ((u8*)rcrb + 0x3800);
for (u32 addr = 0; addr <= 0x1000; addr += 64) {
u16 hsfsts;
hsfsts = *(u16*)((u8*)spirb + 0x04);
// clear FCERR, AEL, FDONE bits
hsfsts &= ~((1 << 2) | (1 << 1) | (1 << 0));
*(u16*)((u8*)spirb + 0x04) = hsfsts;
u32 faddr;
faddr = *(u32*)((u8*)spirb + 0x08);
faddr &= 0x01FFFFFF;
faddr |= addr;
*(u32*)((u8*)spirb + 0x08) = addr;
u16 hsfctl;
hsfctl = *(u16*)((u8*)spirb + 0x06);
hsfctl &= ~(0b11 << 1); // READ request
hsfctl |= ((64 – 1) << 8) | (1 << 0); // FGO, FDBC
*(u16*)((u8*)spirb + 0x06) = hsfctl;
// print FDATAx values
}

---
Reading from the Flash ROM
void *spirb;
spirb = ((u8*)rcrb + 0x3800);
for (u32 addr = 0; addr <= 0x1000; addr += 64) {
u16 hsfsts;
hsfsts = *(u16*)((u8*)spirb + 0x04);
// clear FCERR, AEL, FDONE bits
hsfsts &= ~((1 << 2) | (1 << 1) | (1 << 0));
*(u16*)((u8*)spirb + 0x04) = hsfsts;
u32 faddr;
faddr = *(u32*)((u8*)spirb + 0x08);
faddr &= 0x01FFFFFF;
faddr |= addr;
*(u32*)((u8*)spirb + 0x08) = addr;
u16 hsfctl;
hsfctl = *(u16*)((u8*)spirb + 0x06);
hsfctl &= ~(0b11 << 1); // READ request
hsfctl |= ((64 – 1) << 8) | (1 << 0); // FGO, FDBC
*(u16*)((u8*)spirb + 0x06) = hsfctl;
// print FDATAx values
}
From 0x0000 to 0x1000, 64 byte blocks

---
Reading from the Flash ROM
void *spirb;
spirb = ((u8*)rcrb + 0x3800);
for (u32 addr = 0; addr <= 0x1000; addr += 64) {
u16 hsfsts;
hsfsts = *(u16*)((u8*)spirb + 0x04);
// clear FCERR, AEL, FDONE bits
hsfsts &= ~((1 << 2) | (1 << 1) | (1 << 0));
*(u16*)((u8*)spirb + 0x04) = hsfsts;
u32 faddr;
faddr = *(u32*)((u8*)spirb + 0x08);
faddr &= 0x01FFFFFF;
faddr |= addr;
*(u32*)((u8*)spirb + 0x08) = addr;
u16 hsfctl;
hsfctl = *(u16*)((u8*)spirb + 0x06);
hsfctl &= ~(0b11 << 1); // READ request
hsfctl |= ((64 – 1) << 8) | (1 << 0); // FGO, FDBC
*(u16*)((u8*)spirb + 0x06) = hsfctl;
// print FDATAx values
}
Clear status bits

---
Reading from the Flash ROM
void *spirb;
spirb = ((u8*)rcrb + 0x3800);
for (u32 addr = 0; addr <= 0x1000; addr += 64) {
u16 hsfsts;
hsfsts = *(u16*)((u8*)spirb + 0x04);
// clear FCERR, AEL, FDONE bits
hsfsts &= ~((1 << 2) | (1 << 1) | (1 << 0));
*(u16*)((u8*)spirb + 0x04) = hsfsts;
u32 faddr;
faddr = *(u32*)((u8*)spirb + 0x08);
faddr &= 0x01FFFFFF;
faddr |= addr;
*(u32*)((u8*)spirb + 0x08) = addr;
u16 hsfctl;
hsfctl = *(u16*)((u8*)spirb + 0x06);
hsfctl &= ~(0b11 << 1); // READ request
hsfctl |= ((64 – 1) << 8) | (1 << 0); // FGO, FDBC
*(u16*)((u8*)spirb + 0x06) = hsfctl;
// print FDATAx values
}
Set the address

---
Reading from the Flash ROM
void *spirb;
spirb = ((u8*)rcrb + 0x3800);
for (u32 addr = 0; addr <= 0x1000; addr += 64) {
u16 hsfsts;
hsfsts = *(u16*)((u8*)spirb + 0x04);
// clear FCERR, AEL, FDONE bits
hsfsts &= ~((1 << 2) | (1 << 1) | (1 << 0));
*(u16*)((u8*)spirb + 0x04) = hsfsts;
u32 faddr;
faddr = *(u32*)((u8*)spirb + 0x08);
faddr &= 0x01FFFFFF;
faddr |= addr;
*(u32*)((u8*)spirb + 0x08) = addr;
u16 hsfctl;
hsfctl = *(u16*)((u8*)spirb + 0x06);
hsfctl &= ~(0b11 << 1); // READ request
hsfctl |= ((64 – 1) << 8) | (1 << 0); // FGO, FDBC
*(u16*)((u8*)spirb + 0x06) = hsfctl;
// print FDATAx values
}
READ request, set the block length and go

---
Reading from the Flash ROM
void *spirb;
spirb = ((u8*)rcrb + 0x3800);
for (u32 addr = 0; addr <= 0x1000; addr += 64) {
u16 hsfsts;
hsfsts = *(u16*)((u8*)spirb + 0x04);
// clear FCERR, AEL, FDONE bits
hsfsts &= ~((1 << 2) | (1 << 1) | (1 << 0));
*(u16*)((u8*)spirb + 0x04) = hsfsts;
u32 faddr;
faddr = *(u32*)((u8*)spirb + 0x08);
faddr &= 0x01FFFFFF;
faddr |= addr;
*(u32*)((u8*)spirb + 0x08) = faddr;
u16 hsfctl;
hsfctl = *(u16*)((u8*)spirb + 0x06);
hsfctl &= ~(0b11 << 1); // READ request
hsfctl |= ((64 – 1) << 8) | (1 << 0); // FGO, FDBC
*(u16*)((u8*)spirb + 0x06) = hsfctl;
// print FDATAx values
}
Print, dump ….

---
The Final BIOS Dump File
The FDATAx should contain the actual BIOS data
It can be reverse engineered
The WRITE command can be used to patch some areas
But to keep the malware persistent, we have to understand the internal workings of the BIOS

---
The Flash ROM
SPI FLASH
RESET
16 bytes

---
UEFI vs Legacy BIOS
Unified Extensible Firmware Interface (UEFI) is standardized
EDK II is a generic reference implementation
IBVs and OEMs extend it on their own
UEFI was started in 2005
Nowadays almost every x86 machine has an UEFI firmware installed

---
The Flash Regions
Flash Descriptor
BIOS Region
ME Region
GbE Region

---
The FREGx Registers
They are in SPIRB (RCRB + SPIBAR)
Point to regions in the flash memory
They have predefined meanings
FREG0: Flash Descriptor
FREG1: BIOS Descriptor
FREG2: ME Descriptor
FREG3: GbE Descriptor
FREG4: Platform Data
The special address 0x1FFF indicates that the region is not being used

---
FREGx Registers
Flash Region Register X - 0x54+
31 30 29 28 27 26 25 24 23 22 21 20 19 18 17 16 15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
Region Limit
Region Base
Region Base: needs to be shifted left by 12
Region Limit: needs to be shifted right by 4

---
BOOT Phases
SEC
PEI
DXE
BDS
TSL
RT
AL
Pre Verifier
HW Init
EFI Drivers
Boot Manager
Boot Loader
OS
Power On
OS Boot
Shutdown

---
The Firmware Volumes
Firmware Volume Header
BIOS Region
Firmware File
Firmware File Header
Flash Descriptor
Volume
Firmware File 0
File Section 0
Firmware File Content 0
BIOS Region
Firmware File 1
File Section 1
Firmware File Content 1
ME Region
Volume 0
Volume 1
Volume 1
Firmware File N
GbE Region
Volume N
File Section N
Firmware File Content N

---
Definitions
typedef struct {
UINT8 ZeroVector[16];
EFI_GUID FileSystemGuid;
UINT64 FvLength;
UINT32 Signature;
EFI_FVB_ATTRIBUTES_2 Attributes;
UINT16 HeaderLength;
UINT16 Checksum;
UINT16 ExtHeaderOffset;
UINT8 Reserved[1];
UINT8 Revision;
EFI_FV_BLOCK_MAP BlockMap[];
} EFI_FIRMWARE_VOLUME_HEADER;
typedef struct {
EFI_GUID Name;
EFI_FFS_INTEGRITY_CHECK IntegrityCheck;
EFI_FV_FILETYPE Type;
    EFI_FFS_FILE_ATTRIBUTES Attributes;
    UINT8 Size[3];
    EFI_FFS_FILE_STATE State;
} EFI_FFS_FILE_HEADER;
typedef struct {
UINT8 Size[3];
EFI_SECTION_TYPE Type;
} EFI_COMMON_SECTION_HEADER;
First file can be found at Volume Start + HeaderLength
Consecutive files can be found by moving Size amount
Similarly file sections can be found by using the section Size
The core files are PE or TE formatted files

---
The Result
Entry Point

---
The UEFI Images
Drivers: Stays in the System Memory
Service Drivers: Provides Protocols
Boot Service: Removed after Boot Loader exits
Runtime: Remains after Boot Loader exits
Initialization Drivers: Performs Platform initialization
…
Applications: Cleanup is performed after exit
Boot Loaders: Grub, Winbmgr etc.
EFI Shell Commands: Utility tools
...

---
The UEFI Image Entry
The entry point accepts 2 arguments
The ImageHandle, firmware installed handle
The SystemTable, a pointer to service APIs and more

---
The System Table
typedef struct {
        EFI_TABLE_HEADER Hdr;
        CHAR16 *FirmwareVendor;
        UINT32 FirmwareRevision;
        EFI_HANDLE ConsoleInHandle;
        EFI_SIMPLE_TEXT_INPUT_PROTOCOL *ConIn;
        EFI_HANDLE ConsoleOutHandle;
        EFI_SIMPLE_TEXT_OUTPUT_PROTOCOL *ConOut;
        EFI_HANDLE StandardErrorHandle;
        EFI_SIMPLE_TEXT_OUTPUT_PROTOCOL *StdErr;
        EFI_RUNTIME_SERVICES *RuntimeServices;
        EFI_BOOT_SERVICES *BootServices;
        UINTN NumberOfTableEntries;
        EFI_CONFIGURATION_TABLE *ConfigurationTable;
} EFI_SYSTEM_TABLE;
Runtime APIs
Boot APIs

---
The Runtime Services
typedef struct {
        EFI_TABLE_HEADER Hdr;
        EFI_GET_TIME GetTime;
        EFI_SET_TIME SetTime;
        EFI_GET_WAKEUP_TIME GetWakeupTime;
        EFI_SET_WAKEUP_TIME SetWakeupTime;
        EFI_SET_VIRTUAL_ADDRESS_MAP SetVirtualAddressMap;
        EFI_CONVERT_POINTER ConvertPointer;
        EFI_GET_VARIABLE GetVariable;
        EFI_GET_NEXT_VARIABLE_NAME GetNextVariableName;
        EFI_SET_VARIABLE SetVariable;
        EFI_GET_NEXT_HIGH_MONO_COUNT GetNextHighMonotonicCount;
        EFI_RESET_SYSTEM ResetSystem;
        EFI_UPDATE_CAPSULE UpdateCapsule;
        EFI_QUERY_CAPSULE_CAPABILITIES QueryCapsuleCapabilities;
        EFI_QUERY_VARIABLE_INFO QueryVariableInfo;
} EFI_RUNTIME_SERVICES;
Allows OS to change EFI Vars
Allows updating the Firmware

---
The Boot Services
typedef struct {
    EFI_TABLE_HEADER Hdr;
    ...
    EFI_INSTALL_PROTOCOL_INTERFACE InstallProtocolInterface;
    ...
    EFI_HANDLE_PROTOCOL HandleProtocol;
    ...
    EFI_IMAGE_LOAD LoadImage;
    EFI_IMAGE_START StartImage;
    ...
    EFI_EXIT_BOOT_SERVICES ExitBootServices;
    ...
    EFI_OPEN_PROTOCOL OpenProtocol;
    EFI_CLOSE_PROTOCOL CloseProtocol;
    ...
    EFI_LOCATE_PROTOCOL LocateProtocol;
    ...
} EFI_BOOT_SERVICES;

---
The UEFI Protocols
Serve as Library APIs
There are predefined APIs which can be used at the beginning
Drivers can create their own interfaces
They’re used to abstract away from the hardware
Identified by a GUID
They HAVE to contain the GUID, but Functions and/or Data is optional

---
UEFI Application example
EFI_STATUS EFIAPI UefiMain(
EFI_HANDLE ImageHandle,
EFI_SYSTEM_TABLE *SystemTable)
{
MY_INTERFACE *MyInterface;
SystemTable->BootServices->LocateProtocol(
MY_PROTOCOL_GUID,
NULL,
&MyInterface);
// ...
MyInterface->MyFunction0();
// ...
return EFI_SUCCESS;
}

---
Questions?
LinkedIn: Hrant Tadevosyan, Levon Martirosyan
Email: hrant.tadevosyan@protonmail.com, levonmartirosyan2019@gmail.com
GitHub: https://github.com/0x0000z3r0/bios
Website: astronaut.am